## Slide 1: Course Theme: Abstraction Is Good But Don’t Forget Reality
Carnegie Mellon
CIS courses often emphasize abstraction
  Abstract data types
  Asymptotic analysis
These abstractions have limits
  Need to understand details of underlying implementations
Useful outcomes
  Become effective programmers
    Able to write code that’s easy to reason about
    Able to understand and tune for program performance
    Able to find and eliminate bugs efficiently
  Prepare for later “systems” classes in CIS
    Compilers, Operating Systems, Networks, Computer Architecture, Graphics, Game Programming

## Slide 2: Great Reality #1: Ints are not Integers, Floats are not Reals
Carnegie Mellon
Example 1: Is x2 ≥ 0?
  Float’s: Yes!
  Int’s:
    40000 * 40000 ➙ 1600000000
    50000 * 50000 ➙ ??
Example 2: Is (x + y) + z = x + (y + z)?
  Unsigned & Signed Int’s: Yes!
  Float’s:
    (1e20 + -1e20) + 3.14 --> 3.14
    1e20 + (-1e20 + 3.14) --> ??
Source: xkcd.com/571

## Slide 3: Great Reality #2: You’ve Got to Know Assembly
Carnegie Mellon
Understanding assembly is key to machine-level execution model
  Behavior of programs in presence of bugs
    High-level language models break down
  Tuning program performance
    Understand optimizations done / not done by the compiler
    Understanding sources of program inefficiency
  Implementing system software
    Compiler has machine code as target
    Operating systems must manage process state
  Google says so

## Slide 4: Great Reality #3: Memory Matters Random Access Memory Is an Unphysical Abstraction
Carnegie Mellon
Memory is not unbounded
  It must be allocated and managed
  Many applications are memory dominated
Memory referencing bugs especially pernicious
  Effects are distant in both time and space
Memory performance is not uniform
  Cache and virtual memory effects can greatly affect program performance
  Adapting program to characteristics of memory system can lead to major speed improvements

## Slide 5: Memory Referencing Bug Example
Carnegie Mellon
  Result is system specific
fun(0) ➙ 3.140000
fun(1) ➙ 3.140000
fun(2) ➙ 3.140000
fun(3) ➙ 2.000001
fun(4) ➙ 3.140000
fun(6) ➙ Segmentation fault: 11
typedef struct {
int a[2];
double d;
} struct_t;
double fun(int i) {
struct_t s;
s.d = 3.14;
s.a[i] = 1073741824; /* Possibly out of bounds */
return s.d;
}

## Slide 6: Memory System Performance Example
Carnegie Mellon
Hierarchical memory organization
Performance depends on access patterns
  Including how step through multi-dimensional array
void copyji(int src[2048][2048],
int dst[2048][2048])
{
int i,j;
for (j = 0; j < 2048; j++)
for (i = 0; i < 2048; i++)
dst[i][j] = src[i][j];
}
void copyij(int src[2048][2048],
int dst[2048][2048])
{
int i,j;
for (i = 0; i < 2048; i++)
for (j = 0; j < 2048; j++)
dst[i][j] = src[i][j];
}
81.8ms
4.3ms
2.0 GHz Intel Core i7 Haswell

## Slide 7: Example Memory Hierarchy
Regs
L1 cache
(SRAM)
Main memory
(DRAM)
Local secondary storage
(local disks)
Larger,
slower,
and
cheaper
(per byte)
storage
devices
Remote secondary storage
(e.g., Web servers)
Local disks hold files retrieved from disks
on remote servers
L2 cache
(SRAM)
L1 cache holds cache lines retrieved from the L2 cache.
CPU registers hold words retrieved from the L1 cache.
L2 cache holds cache lines
retrieved from L3 cache
L0:
L1:
L2:
L3:
L4:
L5:
Smaller,
faster,
and
costlier
(per byte)
storage
devices
L3 cache
(SRAM)
L3 cache holds cache lines
retrieved from main memory.
L6:
Main memory holds disk blocks retrieved from local disks.

## Slide 8: Why The Performance Differs
Chart: Stride (x8 bytes)
| s1 | s2 | s3 | s4 | s5 | s6 | s7 | s8 | s9 | s10 | s11
128m | 8350 | 4750 | 3096 | 2286 | 1817 | 1512 | 1293 | 1131 | 1055 | 995 | 945 | 900
64m | 8352 | 4750 | 3092 | 2287 | 1816 | 1510 | 1291 | 1129 | 1051 | 989 | 938 | 894
32m | 8406 | 4787 | 3098 | 2289 | 1823 | 1512 | 1295 | 1133 | 1052 | 989 | 938 | 892
16m | 8556 | 4990 | 3204 | 2376 | 1891 | 1579 | 1356 | 1198 | 1127 | 1070 | 1028 | 994
8m | 8998 | 5447 | 3570 | 2643 | 2104 | 1743 | 1477 | 1300 | 1217 | 1158 | 1128 | 1096
4m | 11494 | 7921 | 5664 | 4319 | 3524 | 2991 | 2592 | 2298 | 2208 | 2148 | 2117 | 2077
2m | 12297 | 8417 | 5940 | 4573 | 3734 | 3174 | 2763 | 2446 | 2349 | 2272 | 2213 | 2160
1024k | 12422 | 8398 | 5971 | 4569 | 3740 | 3172 | 2756 | 2446 | 2351 | 2271 | 2209 | 2162
512k | 12432 | 8472 | 5950 | 4573 | 3726 | 3165 | 2758 | 2447 | 2341 | 2267 | 2210 | 2162
256k | 12564 | 10037 | 8679 | 7175 | 5915 | 5022 | 4345 | 3856 | 3895 | 3981 | 4001 | 4404
128k | 12711 | 10750 | 10271 | 8649 | 7525 | 6374 | 5482 | 4854 | 4901 | 4933 | 4917 | 4924
64k | 12687 | 10689 | 10208 | 8768 | 7570 | 6352 | 5460 | 4830 | 4885 | 4885 | 4823 | 4868
copyij
copyji

## Slide 9: Great Reality #4: There’s more to performance than asymptotic complexity
Carnegie Mellon
Constant factors matter too!
And even exact op count does not predict performance
  Easily see 10:1 performance range depending on how code written
  Must optimize at multiple levels: algorithm, data representations, procedures, and loops
Must understand system to optimize performance
  How programs compiled and executed
  How to measure program performance and identify bottlenecks
  How to improve performance without destroying code modularity and generality

## Slide 10: Example Matrix Multiplication
Carnegie Mellon
Standard desktop computer, vendor compiler, using optimization flags
Both implementations have exactly the same operations count (2n3)
What is going on?
Matrix-Matrix Multiplication (MMM) on 2 x Core 2 Duo 3 GHz (double precision)
Gflop/s
320x
Triple loop
Best code

## Slide 11: MMM Plot: Analysis
Carnegie Mellon
Matrix-Matrix Multiplication (MMM) on 2 x Core 2 Duo 3 GHz
Gflop/s
Memory hierarchy and other optimizations: 20x
Vector instructions: 4x
Multiple threads: 4x
Reason for 20x: Blocking or tiling, loop unrolling, instruction scheduling
Effect: fewer register spills and L1/L2 cache misses

## Slide 12: Great Reality #5: Performance ALWAYS Matters (IMHO)
Carnegie Mellon
Apps
Games
Servers
Web pages
OS
Libs
Can anyone think of a case where performance DOESN’T matter? 