## Slide 1: Floating Point
Carnegie Mellon
Background: Fractional binary numbers
IEEE floating point standard: Definition
Example and properties
Addition, multiplication
Floating point in C

## Slide 2: Fractional binary numbers
Carnegie Mellon
1110011 can represent lots of things
  Positive integer
  Negative integer
  Character in a string
  Color
  Etc.
What is 111.0011?

## Slide 3: Fractional Binary Numbers
2i
2i-1
4
2
1
1/2
1/4
1/8
2-j
bi | bi-1 | ••• | b2 | b1 | b0 | b-1 | b-2 | b-3 | ••• | b-j
Carnegie Mellon
• • •
Representation
  Bits to right of “binary point” represent fractional powers of 2
  Represents rational number:
• • •
Notes: Latex source for equation: \sum_{k=-j}^i b_k \times 2^k

## Slide 4: Fractional Binary Numbers: Examples
Carnegie Mellon
Value Representation
5 3/4 101.112
2 7/8 10.1112
7/16 0.01112
Observations
Divide by 2 by shifting numbers right
Multiply by 2 by shifting numbers left
Numbers of form 0.111111…2 are just below 1.0
  1/2 + 1/4 + 1/8 + … + 1/2i + … ➙ 1.0
  Use notation 1.0 – ε

## Slide 5: Representable Numbers
Carnegie Mellon
Limitation #1
  Can only exactly represent numbers of the form x/2k
    Other rational numbers have repeating bit representations
  Value Representation
    1/3 0.0101010101[01]…2
    1/5 0.001100110011[0011]…2
    1/10 0.0001100110011[0011]…2
Limitation #2
  Just one setting of binary point within the w bits
    Limited range of numbers (very small values? very large?)

## Slide 6: Floating Point
Carnegie Mellon
Background: Fractional binary numbers
IEEE floating point standard: Definition
Example and properties
Addition, multiplication
Floating point in C

## Slide 7: IEEE Floating Point
Carnegie Mellon
IEEE Standard 754
  Established in 1985 as uniform standard for floating point arithmetic
    Before that, many idiosyncratic formats
  Supported by all major CPUs
Driven by numerical concerns
  Nice standards for rounding, overflow, underflow, infinity
  Hard to make fast in hardware
    Numerical analysts predominated over hardware designers in defining standard
    Lots of cases!

## Slide 8: IEEE Floating Point Representation
Carnegie Mellon
How to encode/decode?
Numerical Form: (–1)s M 2E
  Sign bit s determines whether number is negative or positive
  Significand M normally a fractional value in range [1.0,2.0).
  Exponent E weights value by power of two
Encoding
  MSB s is sign bit s
  exp field encodes E (but is not equal to E)
  frac field encodes M (but is not equal to M)
s | exp | frac

## Slide 9: IEEE Precisions
Carnegie Mellon
Single precision: 32 bits
Double precision: 64 bits
Extended precision: 80 bits (Intel only)
s | exp | frac
1 | 8-bits | 23-bits
s | exp | frac
1 | 11-bits | 52-bits
s | exp | frac
1 | 15-bits | 63 or 64-bits

## Slide 10: “Normalized” Values
Carnegie Mellon
When: exp ≠ 000…0 and exp ≠ 111…1
Sign: 0 for positive, 1 for negative
Exponent coded as a biased value: E = Exp – Bias
  Exp: unsigned value of exp field
  Bias = 2k-1 - 1, where k is number of exponent bits
    Single precision: 127 (Exp: 1…254, E: -126…127)
    Double precision: 1023 (Exp: 1…2046, E: -1022…1023)
Significand coded with implied leading 1: M = 1.xxx…x2
  xxx…x: bits of frac field
  Minimum when frac=000…0 (M = 1.0)
  Maximum when frac=111…1 (M = 2.0 – ε)
  Get extra leading bit for “free” because significand is normalized and 1 is the only significant figure in binary
v = (–1)s M 2E

## Slide 11: Normalized Encoding Example
Value: float F = 15213.0;
  1521310 = 111011011011012
  = 1.11011011011012 x 213
Significand
  M = 1.11011011011012
  frac = 110110110110100000000002
Exponent
  E = 13
  Bias = 127
  Exp = 140 = 100011002
Result: 0 10001100 11011011011010000000000
s
exp
frac
v = (–1)s M 2E
E = Exp – Bias

## Slide 12: Denormalized Values
Carnegie Mellon
Condition: exp = 000…0
Exponent value: E = 1 – Bias (instead of E = 0 – Bias)
Significand coded with implied leading 0: M = 0.xxx…x2
  xxx…x: bits of frac
Cases
  exp = 000…0, frac = 000…0
    Represents zero value
    Note distinct values: +0 and –0 (why?)
  exp = 000…0, frac ≠ 000…0
    Numbers closest to 0.0
    Equispaced
v = (–1)s M 2E
E = 1 – Bias

## Slide 13: Special Values
Carnegie Mellon
Condition: exp = 111…1
Case: exp = 111…1, frac = 000…0
  Represents value  (infinity)
  Operation that overflows
  Both positive and negative
  E.g., 1.0/0.0 = −1.0/−0.0 = +, 1.0/−0.0 = −
Case: exp = 111…1, frac ≠ 000…0
  Not-a-Number (NaN)
  Represents case when no numeric value can be determined
  E.g., sqrt(–1),  − ,   0

## Slide 14: Visualization: Floating Point Encodings
Carnegie Mellon
+
−
0
+Denorm
+Normalized
−Denorm
−Normalized
+0
NaN
NaN

## Slide 15: Floating Point
Carnegie Mellon
Background: Fractional binary numbers
IEEE floating point standard: Definition
Example and properties
Addition, multiplication
Floating point in C

## Slide 16: Tiny Floating Point Example
Carnegie Mellon
8-bit Floating Point Representation
  the sign bit is in the most significant bit
  the next four bits are the exponent, with a bias of 7
  the last three bits are the frac
Same general form as IEEE Format
  normalized, denormalized
  representation of 0, NaN, infinity
s | exp | frac
1 | 4-bits | 3-bits

## Slide 17: Dynamic Range (Positive Only)
Carnegie Mellon
s exp frac E Value
0 0000 000 -6 0
0 0000 001 -6 1/8*1/64 = 1/512
0 0000 010 -6 2/8*1/64 = 2/512
…
0 0000 110 -6 6/8*1/64 = 6/512
0 0000 111 -6 7/8*1/64 = 7/512
0 0001 000 -6 8/8*1/64 = 8/512
0 0001 001 -6 9/8*1/64 = 9/512
…
0 0110 110 -1 14/8*1/2 = 14/16
0 0110 111 -1 15/8*1/2 = 15/16
0 0111 000 0 8/8*1 = 1
0 0111 001 0 9/8*1 = 9/8
0 0111 010 0 10/8*1 = 10/8
…
0 1110 110 7 14/8*128 = 224
0 1110 111 7 15/8*128 = 240
0 1111 000 n/a inf
closest to zero
largest denorm
smallest norm
closest to 1 below
closest to 1 above
largest norm
Denormalized
numbers
Normalized
numbers
v = (–1)s M 2E
n: E = Exp – Bias
d: E = 1 – Bias

## Slide 18: Distribution of Values
Carnegie Mellon
6-bit IEEE-like format
  e = 3 exponent bits
  f = 2 fraction bits
  Bias is 23-1-1 = 3
Notice how the distribution gets denser toward zero.
8 values
s | exp | frac
1 | 3-bits | 2-bits

## Slide 19: Distribution of Values (close-up view)
Carnegie Mellon
6-bit IEEE-like format
  e = 3 exponent bits
  f = 2 fraction bits
  Bias is 23-1-1 = 3
s | exp | frac
1 | 3-bits | 2-bits

## Slide 20: Special Properties of the IEEE Encoding
Carnegie Mellon
FP Zero Same as Integer Zero
  All bits = 0
Can (Almost) Use Unsigned Integer Comparison
  Must first compare sign bits
  Must consider −0 = 0
  NaNs problematic
    Will be greater than any other values
    What should comparison yield?
  Otherwise OK
    Denorm vs. normalized
    Normalized vs. infinity

## Slide 21: Interesting Numbers
Carnegie Mellon
Description exp frac Numeric Value
Zero 00…00 00…00 0.0
Smallest Denormalized 00…00 00…01 2– {23,52} x 2– {126,1022}
  Single ≈ 1.4 x 10–45
  Double ≈ 4.9 x 10–324
Largest Denormalized 00…00 11…11 (1.0 – ε) x 2– {126,1022}
  Single ≈ 1.18 x 10–38
  Double ≈ 2.2 x 10–308
Smallest Normalized 00…01 00…00 1.0 x 2– {126,1022}
  Just larger than largest denormalized
One 01…11 00…00 1.0
Largest Normalized 11…10 11…11 (2.0 – ε) x 2{127,1023}
  Single ≈ 3.4 x 1038
  Double ≈ 1.8 x 10308
{single,double}

## Slide 22: Floating Point
Carnegie Mellon
Background: Fractional binary numbers
IEEE floating point standard: Definition
Example and properties
Addition, multiplication
Floating point in C

## Slide 23: FP Multiplication
Carnegie Mellon
(–1)s1 M1 2E1 x (–1)s2 M2 2E2
Exact Result: (–1)s M 2E
  Sign s: s1 ^ s2
  Significand M: M1 x M2
  Exponent E: E1 + E2
Fixing
  If M ≥ 2, shift M right, increment E
  If E out of range, overflow
  Round M to fit frac precision
Implementation
  Biggest chore is multiplying significands

## Slide 24: FP Addition
Carnegie Mellon
(–1)s1 M1 2E1 + (–1)s2 M2 2E2
  Assume E1 > E2
Exact Result: (–1)s M 2E
  Sign s, significand M:
    Result of signed align & add
  Exponent E: E1
Fixing
  If M ≥ 2, shift M right, increment E
  if M < 1, shift M left k positions, decrement E by k
  Overflow if E out of range
  Round M to fit frac precision
(–1)s1 M1
(–1)s2 M2
E1–E2
+
(–1)s M

## Slide 25: Floating Point
Carnegie Mellon
Background: Fractional binary numbers
IEEE floating point standard: Definition
Example and properties
Addition, multiplication
Floating point in C

## Slide 26: Floating Point in C
Carnegie Mellon
C Guarantees Two Levels
  float single precision
  double double precision
Conversions/Casting
  Casting between int, float, and double changes bit representation
  float/double → int
    Truncates fractional part
    Not defined when out of range or NaN: Generally sets to TMin
  int → float
    Exact conversion, as long as int has ≤ 24 bit word size
  int → double
    Exact conversion, as long as int has ≤ 53 bit word size