## Slide 1: Instruction Set Architecture
Assembly Language View
  Processor state
    Registers, memory, …
  Instructions
    addq, pushq, ret, …
    How instructions are encoded as bytes
Layer of Abstraction
  Above: how to program machine
    Processor executes instructions in a sequence
  Below: what needs to be built
    Use variety of tricks to make it run fast
    E.g., execute multiple instructions simultaneously
ISA
Compiler
OS
CPU
Design
Circuit
Design
Chip
Layout
Application
Program

## Slide 2: Y86-64 Processor State
ZF
SF
OF
  Program Registers
    15 registers (omit %r15). Each 64 bits
  Condition Codes
    Single-bit flags set by arithmetic or logical instructions
      ZF: Zero SF:Negative OF: Overflow
  Program Counter
    Indicates address of next instruction
  Program Status
    Indicates either normal operation or some error condition
  Memory
    Byte-addressable storage array
    Words stored in little-endian byte order
RF: Program registers
CC: Condition codes
PC
DMEM: Memory
Stat: Program status
%r8
%r9
%r10
%r11
%r12
%r13
%r14
%rax
%rcx
%rdx
%rbx
%rsp
%rbp
%rsi
%rdi

## Slide 3: Y86-64 Instructions
Format
  1–10 bytes of information read from memory
    Can determine instruction length from first byte
    Not as many instruction types, and simpler encoding than with x86-64
  Each accesses and modifies some part(s) of the program state

## Slide 4: Encoding Registers
Each register has 4-bit ID
  Same encoding as in x86-64
Register ID 15 (0xF) indicates “no register”
  Will use this in our hardware design in multiple places
%rax
%rcx
%rdx
%rbx
0
1
2
3
%rsp
%rbp
%rsi
%rdi
4
5
6
7
%r8
%r9
%r10
%r11
8
9
A
B
%r12
%r13
%r14
No Register
C
D
E
F

## Slide 5: Instruction Example
Addition Instruction
  Add value in register rA to that in register rB
    Store result in register rB
    Note that Y86-64 only allows addition to be applied to register data
  Set condition codes based on result
  e.g., addq %rax,%rsi Encoding: 60 06
  Two-byte encoding
    First indicates instruction type
    Second gives source and destination registers
addq rA, rB
6
0
rA
rB
Encoded Representation
Generic Form

## Slide 6: Arithmetic and Logical Operations
  Refer to generically as “OPq”
  Encodings differ only by “function code”
    Low-order 4 bytes in first instruction word
  Set condition codes as side effect
addq rA, rB
6
0
rA
rB
subq rA, rB
6
1
rA
rB
andq rA, rB
6
2
rA
rB
xorq rA, rB
6
3
rA
rB
Add
Subtract (rA from rB)
And
Exclusive-Or
Instruction Code
Function Code

## Slide 7: Move Operations
  Like the x86-64 movq instruction
  Simpler format for memory addresses
  Give different names to keep them distinct
rrmovq rA, rB
2
0
Register  Register
Immediate  Register
irmovq V, rB
F
rB
3
0
V
Register  Memory
rmmovq rA, D(rB)
4
0
rA
rB
D
Memory  Register
mrmovq D(rB), rA
5
0
rA
rB
D

## Slide 8: Move Instruction Examples
irmovq $0xabcd, %rdx
movq $0xabcd, %rdx
30 82 cd ab 00 00 00 00 00 00
X86-64
Y86-64
Encoding:
rrmovq %rsp, %rbx
movq %rsp, %rbx
20 43
mrmovq -12(%rbp),%rcx
movq -12(%rbp),%rcx
50 15 f4 ff ff ff ff ff ff ff
rmmovq %rsi,0x41c(%rsp)
movq %rsi,0x41c(%rsp)
40 64 1c 04 00 00 00 00 00 00
Encoding:
Encoding:
Encoding:

## Slide 9: Conditional Move Instructions
  Refer to generically as “cmovXX”
  Encodings differ only by “function code”
  Based on values of condition codes
  Variants of rrmovq instruction
    (Conditionally) copy value from source to destination register
rrmovq rA, rB
Move Unconditionally
cmovle rA, rB
Move When Less or Equal
cmovl rA, rB
Move When Less
cmove rA, rB
Move When Equal
cmovne rA, rB
Move When Not Equal
cmovge rA, rB
Move When Greater or Equal
cmovg rA, rB
Move When Greater
2
0
rA
rB
2
1
rA
rB
2
2
rA
rB
2
3
rA
rB
2
4
rA
rB
2
5
rA
rB
2
6
rA
rB

## Slide 10: Jump Instructions
  Refer to generically as “jXX”
  Encodings differ only by “function code” fn
  Based on values of condition codes
  Same as x86-64 counterparts
  Encode full destination address
    Unlike PC-relative addressing seen in x86-64
jXX Dest
7
fn
Jump (Conditionally)
Dest

## Slide 11: Jump Instructions
jmp Dest
7
0
Jump Unconditionally
Dest
jle Dest
7
1
Jump When Less or Equal
Dest
jl Dest
7
2
Jump When Less
Dest
je Dest
7
3
Jump When Equal
Dest
jne Dest
7
4
Jump When Not Equal
Dest
jge Dest
7
5
Jump When Greater or Equal
Dest
jg Dest
7
6
Jump When Greater
Dest

## Slide 12: Y86-64 Program Stack
  Region of memory holding program data
  Used in Y86-64 (and x86-64) for supporting procedure calls
  Stack top indicated by %rsp
    Address of top stack element
  Stack grows toward lower addresses
    Top element is at highest address in the stack
    When pushing, must first decrement stack pointer
    After popping, increment stack pointer
%rsp
•
•
•
Increasing
Addresses
Stack “Top”
Stack “Bottom”

## Slide 13: Stack Operations
  Decrement %rsp by 8
  Store word from rA to memory at %rsp
  Like x86-64
  Read word from memory at %rsp
  Save in rA
  Increment %rsp by 8
  Like x86-64
pushq rA
A
0
rA
F
popq rA
B
0
rA
F

## Slide 14: Subroutine Call and Return
  Push address of next instruction onto stack
  Start executing instructions at Dest
  Like x86-64
  Pop value from stack
  Use as address for next instruction
  Like x86-64
call Dest
8
0
Dest
ret
9
0

## Slide 15: Miscellaneous Instructions
  Don’t do anything
  Stop executing instructions
nop
1
0
halt
0
0

## Slide 16: Y86-64 Instruction Set
Byte
pushq rA
A
0
rA
F
jXX Dest
7
fn
Dest
popq rA
B
0
rA
F
call Dest
8
0
Dest
cmovXX rA, rB
2
fn
rA
rB
irmovq V, rB
3
0
F
rB
V
rmmovq rA, D(rB)
4
0
rA
rB
D
mrmovq D(rB), rA
5
0
rA
rB
D
OPq rA, rB
6
fn
rA
rB
ret
9
0
nop
1
0
halt
0
0
0
1
2
3
4
5
6
7
8
9

## Slide 17: Y86-64 Instruction Set
0
1
2
3
4
5
6
7
8
9
V
D
D
Byte
pushq rA
A
0
rA
F
jXX Dest
7
fn
Dest
popq rA
B
0
rA
F
call Dest
8
0
Dest
cmovXX rA, rB
2
fn
rA
rB
irmovq V, rB
3
0
F
rB
rmmovq rA, D(rB)
4
0
rA
rB
mrmovq D(rB), rA
5
0
rA
rB
OPq rA, rB
6
fn
rA
rB
ret
9
0
nop
1
0
halt
0
0
rrmovq
7
0
cmovle
7
1
cmovl
7
2
cmove
7
3
cmovne
7
4
cmovge
7
5
cmovg
7
6

## Slide 18: Y86-64 Instruction Set
Byte
pushq rA
A
0
rA
F
jXX Dest
7
fn
Dest
popq rA
B
0
rA
F
call Dest
8
0
Dest
cmovXX rA, rB
2
fn
rA
rB
irmovq V, rB
3
0
F
rB
V
rmmovq rA, D(rB)
4
0
rA
rB
D
mrmovq D(rB), rA
5
0
rA
rB
D
OPq rA, rB
6
fn
rA
rB
ret
9
0
nop
1
0
halt
0
0
0
1
2
3
4
5
6
7
8
9
addq
6
0
subq
6
1
andq
6
2
xorq
6
3

## Slide 19: Y86-64 Instruction Set
Byte
pushq rA
A
0
rA
F
jXX Dest
7
fn
Dest
popq rA
B
0
rA
F
call Dest
8
0
Dest
cmovXX rA, rB
2
fn
rA
rB
irmovq V, rB
3
0
F
rB
V
rmmovq rA, D(rB)
4
0
rA
rB
D
mrmovq D(rB), rA
5
0
rA
rB
D
OPq rA, rB
6
fn
rA
rB
ret
9
0
nop
1
0
halt
0
0
0
1
2
3
4
5
6
7
8
9
jmp
7
0
jle
7
1
jl
7
2
je
7
3
jne
7
4
jge
7
5
jg
7
6

## Slide 20: Status Conditions
Mnemonic | Code
ADR | 3
Mnemonic | Code
INS | 4
Mnemonic | Code
HLT | 2
Mnemonic | Code
AOK | 1
  Normal operation
  Halt instruction encountered
  Bad address (either instruction or data) encountered
  Invalid instruction encountered
Desired Behavior
  If AOK, keep going
  Otherwise, stop program execution

## Slide 21: Y86-64 Sample Program Structure
  Program starts at address 0
  Must set up stack
    Where located
    Pointer values
    Make sure don’t overwrite code!
  Must initialize data
init: # Initialization
. . .
call Main
halt
.align 8 # Program data
array:
. . .
Main: # Main function
. . .
call len . . .
len: # Length function
. . .
.pos 0x100 # Placement of stack
Stack:

## Slide 22: Assembling Y86-64 Program
  Generates “object code” file len.yo
    Actually looks like disassembler output
  unix> yas len.ys
  0x054: | len:
  0x054: 30f80100000000000000 | irmovq $1, %r8 # Constant 1
  0x05e: 30f90800000000000000 | irmovq $8, %r9 # Constant 8
  0x068: 30f00000000000000000 | irmovq $0, %rax # len = 0
  0x072: 50270000000000000000 | mrmovq (%rdi), %rdx # val = *a
  0x07c: 6222 | andq %rdx, %rdx # Test val
  0x07e: 73a000000000000000 | je Done # If zero, goto Done
  0x087: | Loop:
  0x087: 6080 | addq %r8, %rax # len++
  0x089: 6097 | addq %r9, %rdi # a++
  0x08b: 50270000000000000000 | mrmovq (%rdi), %rdx # val = *a
  0x095: 6222 | andq %rdx, %rdx # Test val
  0x097: 748700000000000000 | jne Loop # If !0, goto Loop
  0x0a0: | Done:
  0x0a0: 90 | ret

## Slide 23: Simulating Y86-64 Program
  Instruction set simulator
    Computes effect of each instruction on processor state
    Prints changes in state from original
  unix> yis len.yo
  Stopped in 33 steps at PC = 0x13. Status 'HLT', CC Z=1 S=0 O=0
  Changes to registers:
  %rax: 0x0000000000000000 0x0000000000000004
  %rsp: 0x0000000000000000 0x0000000000000100
  %rdi: 0x0000000000000000 0x0000000000000038
  %r8: 0x0000000000000000 0x0000000000000001
  %r9: 0x0000000000000000 0x0000000000000008
  Changes to memory:
  0x00f0: 0x0000000000000000 0x0000000000000053
  0x00f8: 0x0000000000000000 0x0000000000000013

## Slide 24: Overview of Logic Design
Fundamental Hardware Requirements
  Communication
    How to get values from one place to another
  Computation
  Storage
Bits are Our Friends
  Everything expressed in terms of values 0 and 1
  Communication
    Low or high voltage on wire
  Computation
    Compute Boolean functions
  Storage
    Store bits of information

## Slide 25: Computing with Logic Gates
  Outputs are Boolean functions of inputs
  Respond continuously to changes in inputs
    With some, small delay
Voltage
Time
a
b
a && b
Rising Delay
Falling Delay

## Slide 26: Combinational Circuits
Acyclic Network of Logic Gates
  Continously responds to changes on primary inputs
  Primary outputs become (after some delay) Boolean functions of primary inputs
Acyclic Network
Primary
Inputs
Primary
Outputs

## Slide 27: Bit Equality
  Generate 1 if a and b are equal
Hardware Control Language (HCL)
  Very simple hardware description language
    Boolean operations have syntax similar to C logical operations
  We’ll use it to describe control logic for processors
Bit equal
a
b
eq
bool eq = (a&&b)||(!a&&!b)
HCL Expression

## Slide 28: Word Equality
  32-bit word size
  HCL representation
    Equality operation
    Generates Boolean value
b31
Bit equal
a31
eq31
b30
Bit equal
a30
eq30
b1
Bit equal
a1
eq1
b0
Bit equal
a0
eq0
Eq
=
B
A
Eq
Word-Level Representation
bool Eq = (A == B)
HCL Representation

## Slide 29: Bit-Level Multiplexor
  Control signal s
  Data signals a and b
  Output a when s=1, b when s=0
Bit MUX
b
s
a
out
bool out = (s&&a)||(!s&&b)
HCL Expression

## Slide 30: Word Multiplexor
  Select input word A or B depending on control signal s
  HCL representation
    Case expression
    Series of test : value pairs
    Output value for first successful test
Word-Level Representation
HCL Representation
b31
s
a31
out31
b30
a30
out30
b0
a0
out0
int Out = [
0 : A;
1 : B;
];
s
B
A
Out
MUX

## Slide 31: Arithmetic Logic Unit
OF
ZF
CF
OF
ZF
CF
OF
ZF
CF
OF
ZF
CF
  Combinational logic
    Continuously responding to inputs
  Control signal selects function computed
    Corresponding to 4 arithmetic/logical operations in Y86-64
  Also computes values for condition codes
A
L
U
Y
X
X + Y
0
A
L
U
Y
X
X - Y
1
A
L
U
Y
X
X & Y
2
A
L
U
Y
X
X ^ Y
3
A
B
A
B
A
B
A
B

## Slide 32: Storing and Accessing 1 Bit
Q+
Q–
R
S
R-S Latch
Resetting
1
0
1
0
0
1
Setting
0
1
0
1
1
0
Storing
0
0
!q
q
q
!q
Bistable Element
Q+
Q–
q
!q
q = 0 or 1

## Slide 33: Registers
  Stores word of data
    Different from program registers seen in assembly code
  Collection of edge-triggered latches
  Loads input on rising edge of clock
I
O
Clock
D
C
Q+
D
C
Q+
D
C
Q+
D
C
Q+
D
C
Q+
D
C
Q+
D
C
Q+
D
C
Q+
i7
i6
i5
i4
i3
i2
i1
i0
o7
o6
o5
o4
o3
o2
o1
o0
Clock
Structure

## Slide 34: Random-Access Memory
  Stores multiple words of memory
    Address input specifies which word to read or write
  Register file
    Holds values of program registers
    %rax, %rsp, etc.
    Register identifier serves as address
      ID 15 (0xF) implies no read or write performed
  Multiple Ports
    Can read and/or write multiple words in one cycle
      Each has separate address and data input/output
Register
file
A
B
W
dstW
srcA
valA
srcB
valB
valW
Read ports
Write port
Clock

## Slide 35: Building Blocks
Combinational Logic
  Compute Boolean functions of inputs
  Continuously respond to input changes
  Operate on data and implement control
Storage Elements
  Store bits
  Addressable memories
  Non-addressable registers
  Loaded only as clock rises
Register
file
A
B
W
dstW
srcA
valA
srcB
valB
valW
Clock
A
L
U
fun
A
B
MUX
0
1
=
Clock