## Slide 1: Today
Storage technologies and trends
Locality of reference
Caching in the memory hierarchy

## Slide 2: Caches
Cache: A smaller, faster storage device that acts as a staging area for a subset of the data in a larger, slower device.
Fundamental idea of a memory hierarchy:
  For each k, the faster, smaller device at level k serves as a cache for the larger, slower device at level k+1.
Why do memory hierarchies work?
  Because of locality, programs tend to access the data at level k more often than they access the data at level k+1.
  Thus, the storage at level k+1 can be slower, and thus larger and cheaper per bit.
Big Idea: The memory hierarchy creates a large pool of storage that costs as much as the cheap storage near the bottom, but that serves data to programs at the rate of the fast storage near the top.

## Slide 3: General Cache Concepts: Hit
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
8
9
14
3
Cache
Memory
Data at address is needed
Request: 14
14
Data is in cache:
Hit!

## Slide 4: General Cache Concepts: Miss
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
8
9
14
3
Cache
Memory
Data at address is needed
Request: 12
Data is not in cache:
Miss!
Data is fetched from
memory
Request: 12
12
12
12
Data is stored in cache
Replacement policy: determines which block gets evicted (victim)

## Slide 5: General Cache Organization (S, E, B)
E = 2e lines per set
S = 2s sets
set
line
0
1
2
B-1
tag
v
B = 2b bytes per cache block (the data)
Cache size:
C = S x E x B data bytes

## Slide 6: Decoding Addresses
Every byte in memory belongs to a block:
  Lowest order o “offset” bits specify the byte’s position in its block
Each block belongs to a set in the cache:
  Next lowest order s “set” bits specify the cache set to which the block belongs
Many many blocks in memory will belong to the same cache set, so we need a way to identify cached blocks:
  Remaining t “tag” bits are used to determine if a cached block is the block containing the desired byte
t bits
s bits
o bits
Address: